GSC-Ottawa Polygon Model FileFormat: Jim Craven & Alan Jones
============================================================
Version 1.0: 17 Feb 1992


A Simple Polygon File Format for Model Interchange
--------------------------------------------------

A polygon file format is proposed for model interchange for the
following reasons:

1.  the polygon format is easily plotted and programs exist to
      accomplish this using X Windows and Uniras.

2.  any number of parameters such as conductivity or density
      may be associated with each polygon.

3.  provides a simple basis for conversion to model formats for
      use in forward modeling programs.

4.  programs exist to convert Madden's EMCDC model files, Wannamaker's 
      PW2D model files, and OCCAM2 output model files to the polygon 
      format (model->ply).

5.  program are under development to convert the polygon files to
      input model files to the above, and other, 2D modelling codes
      (ply->model).


At present, the polygon format proposed satisfies the requirements of
only 1D or 2D modeling. A keyword in the title line could specify that
the polygons are fully 3D and three coordinates would be read in for
every vertex. 

The Ottawa polygon file is composed of two parts: the header and polygon 
information, both of which are formed with 7-bit ASCII bytes, i.e., 
readable by any standard editor. The header is the first three lines 
(or records) in the file.  These lines may contain keywords and values 
associated with those keywords that may be used in plot scaling or 
annotating etc.  

The polygon information starts on the 4th line with parameters 
associated with a half-space.  The following records refer to polygons
that either tile or overlap upon the half-space (note overlap rule
specified below).


--------------------------------------------------------------------------------

Header Information (3 lines)
----------------------------

The first line contains a string either for use as a plot
title or to refer to the original model file that was
converted to a polygon file.  The key character ``>'' appearing in
this first line indicates the next 4 characters are the azimuth of the
survey line.  Another key, ``PRF='' indicates the next string is a 
filename containing site easting and northing information.  The keys
are separated from the title string with a ``!'' character.

For example, the first header line may appear as:

Model No 1.5 !>-020 PRF=line8.prf

which specifies model number 1.5 of the station listed
in line8.prf rotated to an azimuth of -20 degrees.

The second and third line are x- and y-axis label information
respectively and generally appear as 

Distance (km)
Log (Depth [km])

The distances in the polygon file should all be in metres but the
keywords ``km'' and ``Log'' indicate that the distances should
be scaled appropriately for plotting purposes.

--------------------------------------------------------------------------------

The Half-Space
--------------

The fourth line in the file specifies the location and parameters
of a half-space on which the subsequent polygons are to be tiled
or overlapped.

An example half-space record is:

000  100000  5550000  1   1000.000   'RES'

Note that the fields in this record are all being read using 
FORTRAN free-format. 
 
The first field is a polygon id which is normally 0.  

The second and third fields are the model bind point expressed as
an easting and northing.  When coupled with the azimuth, this bind point 
fixes the model in space.  

The next field specifies the number of parameters associated with the 
half-space; in this case there is only one parameter.  

The remaining fields are pairs of parameter values and free format 
character parameter labels.  There is only one pair in this case, the actual 
half-space  parameter value (100 ohm.m) and the 'RES' label indicating the 
parameter is in fact a resistivity. 

If the model file specifies both resistivities and densities for the half 
space and for the polygons, then an example half-space record would be:

  0  100000  5550000  2   1000.0   'RES'     2890.0  'DENS'

(NOTE: all units in the file shoudl be in S.I.)


--------------------------------------------------------------------------------

The Polygons
------------

Subsequent pairs of records in the polygon file describe individual
polygons.  The fields in both records are purely numerical and are read in 
using free format integer and real reads. 

An example is:

001 4 1    10358.6
      0.      0.      44000.      0.      44000.   1000.          0.   1000.
 

The first record for a particular polygon specifies the id (001), number of 
vertices (4), number of parameters (1) and the parameter values (10358.6). The 
parameter labels are not given as they are assumed to be the same as for the
half-space and in the same order.  

The second record is a clockwise list of y-z pairs of the vertex locations for 
that polygon. The y-z vertex values are determined using the following rules:

y: the y coordinate is specified as an offset along the 
      profile azimuth from the bind point specified in the half-space record
z: the z value specifies depth and increases downward
 
The units, as has already been mentioned, are metres. The special y-coordinates
-1.e32 and +1.e32 denote minus (most westerly) and plus (most easterly or deepest) 
infinity respectively. Thus a layer across the model space can be specified, e.g., 
for a 10 ohm.m layer from 10-15 km.

022 4 1    10.
      -1.e32 10000.      1.e32 10000.      1.e32 15000.      -1.e32 10000.



The Enf-of-file mark ends input - there is nowhere specified how many
polygons need to be read in. Also, the polygon id numbers need not be sequential
nor need they be complete. So you can easily delete a polygon or add another
out-of-sequence using a text editor (the overlap rule applies).

Overlap Rule:
-------------
In the case of overlapping polygons, the last specified takes precidence.


--------------------------------------------------------------------------------

Sample polygon file
-------------------

The following is a complete polygon file specifying a 1000 ohm.m
half-space and 10 polygons that do not overlap.


OCCAM2 files: l18.grid3;inmodel3;model16; !>0090 PRF=l18.prf
Distance (km)
Depth (km)
  0  100000  5550000  1   1000.000  'RES'
001 4 1    10358.6
      0.      0.      44000.      0.      44000.   1000.          0.   1000.
002 4 1     6395.9
  44000.      0.      46000.      0.      46000.   1000.      44000.   1000.
003 4 1     4213.1
  46000.      0.      48000.      0.      48000.   1000.      46000.   1000.
004 4 1     3384.5
  48000.      0.      50000.      0.      50000.   1000.      48000.   1000.
005 4 1     3476.2
  50000.      0.      52250.      0.      52250.   1000.      50000.   1000.
006 4 1      840.6
  52250.      0.      54500.      0.      54500.   1000.      52250.   1000.
007 4 1     4020.7
  54500.      0.      56000.      0.      56000.   1000.      54500.   1000.
008 4 1     7906.8
  56000.      0.      58000.      0.      58000.   1000.      56000.   1000.
009 4 1    10651.2
  58000.      0.      60000.      0.      60000.   1000.      58000.   1000.
010 4 1    10034.6
  60000.      0.      62000.      0.      62000.   1000.      60000.   1000.




--------------------------------------------------------------------------------

If you have any questions/problems/suggestions, please contact either of us.
All the translation/plotting codes are available on request.

Jim Craven & Alan Jones
Geological Survey of Canada
1 Observatory Crescent
Ottawa, Ontario,
CANADA  K1A 0Y3

tel: (613) 992-8242 (Jim)   or    (613) 992-4968 (Alan)
FAX: (613) 992-8836
email: craven@cg.nrcan.gc.ca     or    ajones@nrcan.gc.ca